PLUVIÓMETRO
modelo: aceiro inox
Saída: RS485

key technical indicators

Diameter of bearing rain: φ200mm; sharp edge angle: 40 ° ~ 45 °
Resolution: default 0.2 mm, optional 0.1/0.5 mm
Typical accuracy: ≤ ± 4% (indoor precipitation, based on instrument displacement)
Rainfall intensity range: 0mm ~ 4mm/min (maximum rainfall intensity allowed is 8mm/min)
Communication: 485 communication (standard ModBus-RTU protocol)
Power supply: 4.5 ~ 30V Max Power Consumption: 0.24 W working environment:
Ambient Temperature: 0-55 ° C RH: < 95% RH (40 ° C)

sensor wiring

Line color	Description	Line color	Description
Brown Line	The power supply is positive	Yellow Wire	485A
Black line	The power supply is negative	Blue Wire	485B

Con Modbus Poll cada pulso se ve que incrementa 2 unidades. As medidas que entrega o pluviómetro no rexistro Modbus é x10, polo que na figura aparece 12, que equivale a un acumulado de 1,2 mm (neste exemplo déronse 6 pulsos no pluviómetro).

Control desde ESP32 usando conversor RS485-TTL: